## Slide 1: Assessment of Benthic Ecosystem Changes Post-Outplanting Using Structure-from-Motion (SfM) Photogrammetry
Authors: Ian Combs; Gabrielle D’Alonzo*; Erinn Muller; Erich Bartels; Jason Spadaro

## Slide 2: *Introduction
Numerous factors severely affecting the health and diversity of the Florida Reef Tract (FRT)
Disease
Thermal stress
Competition
Ocean acidification
Predation
Coral Restoration is a widely accepted tool used to mitigate the damage affecting the benthic community

## Slide 3: Monitoring Success
Post-restoration:
Fate-tracking via in-water surveys used to monitor success and health in the months → years after outplanting
What SfM photogrammetry can aid in:
  Label loss (physically or result of overgrowth)
  Percent cover & growth metrics
  Whole ecosystem assessment
SfM Photogrammetry has become an increasingly popular monitoring and surveying research aid

## Slide 4: This Project
Ongoing, long-term restoration monitoring study
To date, 39(keep up, to date*) unique reef ledges
  Imaged pre-restoration, and then at 12 months post-restoration
  Imaging is repeated annually going forward
Depending on site, either A. cervicornis of A. palmata was species outplanted
Map of sites?
Objectives
How is the benthic ecosystem shifting post-restoration
How can SfM Photogrammetry assist/streamline answering ecological questions

## Slide 5: Image Acquisition
Site set-up:
Scale bars (also acting as depth markers) placed throughout site
Float markers are placed surrounding target site for orientation aid
Cameras:
Camera rig consists of two GoPro 10s set 60cm apart on a PVC rig
Methods:
Photos are taken with a goal of 80% overlap
Cameras capture 1 image/second
Swim path akin to lawnmower pattern, with a few passes in the perpendicular direction
  Helps reduce reprojection error
Senior Biologist Ian Combs, taken by Staff Scientist/Program Manager Erich Bartels

## Slide 6: SfM Photogrammetry
Imaging technique in which three-dimensional structures are derived from sequences of two-dimensional images
Three-dimensional sparse cloud
Three-dimensional dense cloud
Orthoprojection generated in Viscore
After imagery is taken at target reef site, they are uploaded to Agisoft Metashape
Markers are detected and photos are aligned into a sparse cloud of extracted points
Dense point cloud is then generated
Imagery is used to further rectify point cloud
Software utilizes algorithm to match pixels to pre-existing points
Dense cloud can then be exported to viscore for further annotation and data extraction

## Slide 7: Data Collection
Viscore
software platform which allows for interaction with 3D visual products
Imagery is correctly scaled and oriented
Visual Point Intercept (VPI) survey; automated distribution of randomized points within specified space
  Points are linked to raw imagery for identification
  Determine benthic species composition
SfM photogrammetry allows for analysis with greater detail, without time constraints in-water

## Slide 8: Data Collection
TagLab
AI-powered 2D segmentation software
Combination of semi-automatic tools along with machine-learning capabilities
  Accurate representation of the distribution of 2D reef space between organisms
  Automatic segmentation/classifier tool can be trained to fit different species/reef types
  Both continue to keep operator “in the loop”
AI powered machine-learning capabilities help optimize data extraction

## Slide 9: data

## Slide 10: data/discussion

## Slide 11: Bring it back tg

## Slide 12: Acknowledgements